## Slide 1: Process Planning and Cost Estimation
CME396 | Unit 3: Introduction to Cost Estimation
Important 2-mark and 13-mark questions with answers
Based on Apr/May 2024, Nov/Dec 2024, Apr/May 2025 and Nov/Dec 2025 papers

## Slide 2: Part A
10 two-mark questions with answers

## Slide 3: Importance of cost estimation
1
Why is cost estimation important? What is its purpose? (AM 2024, AM 2025)
Cost estimation is the process of finding the probable cost of a product before it is manufactured. Its purposes are:
To fix the selling price and submit quotations / tenders.
To take make-or-buy decisions and select the most economical process.
To prepare budgets and control the cost of production.
To check whether the product will be profitable before investing.

## Slide 4: Estimation vs costing
2
Compare estimation and costing. (ND 2025)
Point | Estimation | Costing
Meaning | Probable cost | Actual cost
When | Before production | During / after production
Done by | Estimator (technical person) | Cost accountant
Based on | Drawings, past data, judgement | Actual bills, wages, records
Used for | Fixing price, quotations | Controlling cost, finding actual profit

## Slide 5: Elements of cost
3
List the elements of cost. (AM 2025)
M
Material
Direct material
Indirect material
L
Labour
Direct labour
Indirect labour
E
Expenses
Direct expenses
Indirect expenses (overheads)
Overheads = Indirect material + Indirect labour + Indirect expenses; classified as factory, administrative, and selling & distribution overheads.

## Slide 6: Administrative expenses
4
Brief the term administrative expenses. (ND 2024)
Administrative expenses are the costs of running the office (not the shop floor). They are added to the factory cost to get the production (office) cost.
Examples:
Salaries of manager and office staff
Office rent, lighting and insurance
Stationery, postage and telephone
Legal and audit fees

## Slide 7: Methods of allocating overheads
5
List out various methods of allocation of overhead expenses. (AM 2024, ND 2025)
Percentage of direct material cost
Percentage of direct labour cost
Percentage of prime cost
Man-hour rate method
Machine-hour rate method
Combination of man-hour and machine-hour rates
Unit rate method

## Slide 8: Overhead by unit rate method
6
A concern produces 600 machines per year. Total overheads were Rs. 1,80,000. Calculate the overhead cost per machine by unit rate method. (ND 2024)
Overhead per machine =
Total overheads
Number of units produced
=
1,80,000
600
= Rs. 300 per machine

## Slide 9: Man-hour rate and machine-hour rate
7
Define man hour and machine hour rate. (ND 2024)
Man-hour rate
Man-hour rate =
Total factory overheads
Total man-hours worked
Machine-hour rate
Machine-hour rate =
Total cost of running the machine
Total machine hours
Man-hour rate is used where work is mainly manual; machine-hour rate is used where work is mainly done on machines.

## Slide 10: Depreciation
8
Define depreciation. List its methods. (Frequently asked)
Depreciation is the permanent decrease in the value of an asset with time due to wear and tear, age or obsolescence.
Methods:
Straight line method
Reducing balance method
Sinking fund method
Sum-of-years' digits method
Machine-hour basis method

## Slide 11: Prime cost and factory cost
9
Define prime cost and factory cost. (Frequently asked)
Prime cost
Prime cost = Direct material + Direct labour + Direct expenses
Factory cost
Factory cost = Prime cost + Factory overheads
Prime cost is the total of all direct costs; factory (works) cost adds the indirect costs of the factory.

## Slide 12: Direct vs indirect material
10
Differentiate direct and indirect material. (Frequently asked)
Direct material | Indirect material
Becomes a part of the finished product | Helps production but is not part of the product
Can be traced to a particular job | Cannot be traced to a particular job
Charged directly to the job | Charged as overhead
Example: steel bar for a shaft, castings | Example: lubricants, cotton waste, grinding wheels

## Slide 13: Part B
6 thirteen-mark questions with answers

## Slide 14: Q1 · Cost estimation procedure
Q1
Explain the step by step procedure for doing cost estimation for a new product. (ND 2024 – 13a)
D
Definition
Estimation is the technical process of finding the probable cost of a product before production starts, using its drawings and specifications.
Aims of estimation
Fix the selling price; submit quotations / tenders
Decide whether to make or buy a component
Choose the most economical method and machine
Prepare budgets and check profitability

## Slide 15: Q1 · Procedure (contd.)
Study the drawing – material, dimensions, tolerances, finish, quantity
Bill of materials – every part, bought-out items, quantities
Material cost – volume → weight (× density) → + allowances → × rate per kg
Sequence of operations – turning, drilling, milling, welding …
Time per operation – set-up + machining + handling + allowances
Labour cost – time × wage rate per hour
Direct expenses – special tools, jigs, patterns, royalties
Prime cost = material + labour + direct expenses
Add overheads – factory → administrative → selling & distribution
Add profit – total cost + profit = selling price

## Slide 16: Q1 · Example – cast iron pulley
Item | Working | Rs.
Material | 5 kg × Rs. 80 per kg | 400
Labour | 2 h × Rs. 150 per h | 300
Direct expenses | Share of pattern cost | 50
Prime cost | 400 + 300 + 50 | 750
Factory overhead | 40% of labour | 120
Administrative + selling overhead | 60 + 70 | 130
Total cost | 750 + 120 + 130 | 1,000
Selling price | 1,000 + 15% profit | 1,150
Conclusion: an accurate estimate lets the firm quote competitive prices, avoid losses on orders and control production cost.

## Slide 17: Q2 · Elements of cost
Q2
Explain the elements of cost and the ladder of cost. Calculate prime cost, factory cost, production cost, total cost and selling price per item. (AM 2025, ND 2025 – 13a)
M
Material
Direct – part of product (steel bar, castings)
Indirect – oil, cotton waste, small tools
L
Labour
Direct – turner, welder, fitter
Indirect – supervisor, storekeeper, inspector
E
Expenses
Direct – special jigs, patterns, royalty
Indirect (overheads) – rent, power, depreciation

## Slide 18: Q2 · Ladder of cost
Prime cost = Direct material + Direct labour + Direct expenses
Factory cost = Prime cost + Factory overheads
Production cost = Factory cost + Administrative overheads
Total cost = Production cost + Selling & distribution overheads
Selling price = Total cost + Profit
Prime cost
Direct material
Direct labour
Direct expenses
Factory cost
Prime cost
Factory overhead
Production cost
Factory cost
Admin. overhead
Total cost
Production cost
Selling & distribution
Selling price
Total cost
Profit
Shaded = cost so far; gold = cost added at each step

## Slide 19: Q2 · Problem (ND 2025) – solution
Given | Rs.
Raw material stock 01-04-2023 | 25,000
Raw material purchased | 40,000
Raw material stock 31-03-2024 | 15,000
Direct labour | 14,000
Direct expenses | 1,000
Factory overhead | 9,750
Administrative expenditure | 6,500
Selling and distribution | 3,250
Items produced | 650
Profit | 10% of total cost
Step | Working | Total | Per item
Material consumed | 25,000 + 40,000 − 15,000 | 50,000 | 76.92
Prime cost | 50,000 + 14,000 + 1,000 | 65,000 | 100.00
Factory cost | 65,000 + 9,750 | 74,750 | 115.00
Production cost | 74,750 + 6,500 | 81,250 | 125.00
Total cost | 81,250 + 3,250 | 84,500 | 130.00
Profit (10%) | 0.10 × 130 | 8,450 | 13.00
Selling price | 130 + 13 | 92,950 | 143.00
Answer: Selling price = Rs. 143 per item

## Slide 20: Q3 · Material cost estimation
Q3
Explain the steps involved in estimating labour and material costs in manufacturing. (AM 2025 – 13a)
Divide the component into simple shapes (cylinders, prisms, cones).
Find the volume of each shape and add them (subtract holes).
Weight = Volume × Density (steel 7.86 g/cm3, cast iron 7.2 g/cm3, aluminium 2.7 g/cm3).
Add allowances – machining, sprue / scrap, cutting (kerf) and scale losses.
Material cost = Gross weight × Rate per kg + bought-out parts − scrap value.
Material cost = (Volume × Density + Allowances) × Rate per kg − Scrap value

## Slide 21: Q3 · Labour cost estimation
List the operations from the process sheet.
Find set-up time, operation (machining) time and handling time for each operation.
Add 10–20% allowance for fatigue, personal needs, tool sharpening and delays.
Time per piece =
Set-up time
Batch size
+ Operation time + Handling time + Allowances
Labour cost = Total time × Wage rate per hour
Example: 12 min turning + 3 min handling + 15% allowance = 15 × 1.15 = 17.25 min. At Rs. 120 per hour:
Labour cost =
17.25
60
× 120 = Rs. 34.50 per piece

## Slide 22: Q4 · Overheads and their classification
Q4
Describe overheads and the methods of allocating overhead charges in cost estimation. (AM 2024, AM 2025 – 13b, ND 2025)
Overheads are all indirect costs – indirect material, indirect labour and indirect expenses – that cannot be charged directly to one job, so they are shared out fairly.
Type | Examples
Factory (works) | Factory rent, power, lighting, repairs, machine depreciation, supervisor salary
Administrative (office) | Office staff salaries, office rent, stationery, telephone, audit fees
Selling | Advertisement, salesmen's salary and commission, showroom expenses
Distribution | Packing, warehouse rent, transport and delivery vans

## Slide 23: Q4 · Methods of allocation (1–4)
1. % of direct material
% Overhead =
Total overheads
Total direct material cost
× 100
2. % of direct labour
% Overhead =
Total overheads
Total direct labour cost
× 100
3. % of prime cost
% Overhead =
Total overheads
Total prime cost
× 100
4. Man-hour rate
Man-hour rate =
Total overheads
Total man-hours

## Slide 24: Q4 · Methods of allocation (5–7)
5. Machine-hour rate
Machine-hour rate =
Total machine running cost
Total machine hours
6. Combination of man-hour and machine-hour rates – used where both men and machines are important.
7. Unit rate
Overhead per unit =
Total overheads
Number of units produced
Example: overhead Rs. 50,000 and direct labour Rs. 1,00,000 give 50% of labour; a job with Rs. 2,000 labour is charged Rs. 1,000.
Conclusion: the machine-hour rate is the most accurate in machine shops, because most overheads are caused by machines.

## Slide 25: Q5 · Depreciation
Q5
Explain depreciation, its causes and methods, with a note on appreciation. Solve the given problems. (ND 2024 – 13b, ND 2025 – 13b)
D
Depreciation
Permanent decrease in the value of an asset with time.
Charged as a cost so money is available to replace the asset at the end of its life.
Causes
Wear and tear due to use
Age and decay (rust, corrosion)
Obsolescence – better machines available
Accidents, breakdowns, fall in demand
Appreciation is the increase in an asset's value with time (land, buildings in growing cities). Example: a plot bought for Rs. 10 lakh may be worth Rs. 15 lakh after 5 years.

## Slide 26: Q5 · Methods of depreciation
C = initial cost, S = scrap value, n = life in years, i = interest rate
1. Straight line
D =
C − S
n
2. Reducing balance
r = 1 −
(
S
C
)
1/n
Value after m years = C(1 − r)m
3. Sinking fund
A = (C − S) ×
i
(1 + i)n − 1
4. Sum-of-years' digits
Dk = (C − S) ×
n − k + 1
n(n + 1) / 2
5. Machine-hour basis
D per hour =
C − S
Total working hours in life

## Slide 27: Q5 · Problem (i): reducing balance method
A machine costs Rs. 25,000, life 20 years, scrap value Rs. 4,000. Find the depreciation fund after 3 years, depreciation for the 3rd year and the yearly percentage reduction. (7 marks)
r = 1 −
(
4,000
25,000
)
1/20
= 1 − (0.16)0.05 = 1 − 0.9124 = 0.0876 = 8.76%
Year | Value at start (Rs.) | Depreciation @ 8.76% (Rs.) | Value at end (Rs.)
1 | 25,000.00 | 2,188.90 | 22,811.10
2 | 22,811.10 | 1,997.24 | 20,813.86
3 | 20,813.86 | 1,822.33 | 18,991.53
Fund after 3 years = Rs. 6,008.47
3rd-year depreciation = Rs. 1,822.33
Reduction = 8.76% per year
Using logs: log 0.16 = −0.7959; × 0.05 = −0.0398; antilog = 0.9124. Fund = 25,000 − 18,991.53 = 6,008.47

## Slide 28: Q5 · Problem (ii): machine-hour basis
A shaper costs Rs. 85,000, life 8 years, scrap value Rs. 8,500, and works 3,330 hours a year. Find the depreciation per hour and per year. (6 marks)
Total hours = 8 × 3,330 = 26,640 h
Depreciation per hour =
85,000 − 8,500
26,640
=
76,500
26,640
= Rs. 2.87 per hour
Annual depreciation = 2.8716 × 3,330 = Rs. 9,562.50 per year (11.25% of cost)

## Slide 29: Q6 · Methods of costing
Q6
Discuss the methods of costing such as job costing, process costing and activity-based costing, highlighting their differences. (AM 2024 – 13a)
Job costing – each job / order costed separately (repair shops, special machines)
Batch costing – a batch of identical items is one job; cost per item = batch cost ÷ items
Process costing – product passes through processes in sequence (cement, sugar, steel)
Unit costing – one standard product in bulk (bricks, cement bags, mining)
Operating costing – services: transport (per km), power (per kWh)
Contract costing – long works: buildings, bridges, ships
Activity-based costing – overheads traced to activities (set-up, inspection, handling) and charged by usage

## Slide 30: Q6 · Comparison of costing methods
Point | Job costing | Process costing | Activity-based costing
Type of product | Made to order, different each time | Continuous, identical | Many products, high overheads
Cost unit | One job | One process / period | One activity
Overhead charged | Broad rate | Per process | Per activity (cost driver)
Accuracy | Moderate | Average cost only | High
Example | Machine repair | Cement plant | Auto parts plant, many models
Conclusion: job costing suits job-order shops, process costing suits continuous production, and ABC gives the most accurate product costs in modern multi-product factories.

## Slide 31: Exam tips
Write the formula first, then substitute – it earns step marks
Show every numerical step in a table; write units (Rs., hours, %)
Draw the ladder of cost in any cost question